## Slide 1: Health and Safety Investments to Increase Energy-Saving Opportunities
Deb Davis, Columbia Gas
Jackie Berger, APPRISE
National Energy & Utility Affordability Coalition Conference
June 26, 2018

## Slide 2: Presentation Overview
2
Assessing the Problem
Current Health and Safety Investments
Potential Savings for Homes with Health and Safety Problems
LIURP Savings Results
Decision Framework for Additional Health and Safety Investments
Columbia Gas LIURP Background
LIURP Health & Safety Approach

## Slide 3: Columbia Gas of Pennsylvania
Serve 26 counties
Roughly 380,000 residential customers
Census Data – 100,000 low income
Mandated Universal Service Programs
3

## Slide 4: Columbia LIURP
Low Income Usage Reduction Program
Mandated in 1988
Spending & Production Increases
Primary metrics – Production Goals & Savings
4

## Slide 5: LIURP Production
Current Budget $4,750,000
500 – 550 homes completed
Company administered
Contractor installed measures
5

## Slide 6: Production Issue
Ratio of Referral to Completion decreasing
>2000 pre screens to reach production goals
Review of Reasons & Analysis
Bottom Line = Housing Conditions preventing Weatherization and limited (no) funding resources
6

## Slide 7: Health & Safety Deep Dive
High Deferral rate
Been walking away for 20 years
High cost of Deferred jobs
No Wx = Continued High CAP bill subsidy
7

## Slide 8: Current H&S Approach
Fixed CAP on H&S costs per job
Soft CAP on total spend per job
Contractor determines deferral decisions
Average deferral rate – greater than 50%
8

## Slide 9: Assessing the problem
9

## Slide 10: APPRISE
Nonprofit Research Institute
Mission
Research Areas
Clients
Federal Government (DOE, HHS)
State Governments
Utility Companies
Nonprofits
Energy Efficiency
Energy Affordability
Princeton, NJ
Established in 2002
Analyze data and information to assess and improve public programs
10

## Slide 11: Low-Income EE Challenge
11
Low-Income Energy Efficiency
  Increased challenges serving households
  Significant health and safety issues
  Prevent installation of major measures
  Lost potential for high-usage customers
Where/when can additional cost-effective health and safety investments be made?

## Slide 12: Assessing the Problem Methodology
12
Analyze 2015 LIURP Database
Review cancelled job spreadsheet
Review job paperwork
Initial indicators of health and safety issues that prevented work
  No measure or invoice data
  Job marked as incomplete
  No blower door test data
  Blower door indicator marked as not conducted

## Slide 13: Jobs with Potential H&S Issues
13
Chart: Percentage of 2015 Jobs with Potential H&S Issues
| No Invoice Data | Incomplete Job | No Blower Door Test | Blower Door Indicator = 0 | Any of Four Issues Listed
Indicator of Potential Issue | 0.23 | 0.39 | 0.4 | 0.38 | 0.46

## Slide 14: Jobs with Potential H&S Issues
14
Chart: Percentage of 2015 Jobs with Limited Job Costs
| Total Job Costs <$750 | Non-Heating Replacement Job Costs <$750 | Either Cost Issue
Cost Issue | 0.33 | 0.35 | 0.35

## Slide 15
15
Chart: Percentage of 2015 Jobs with Potential H&S Issues All Analysis Factors
| No Invoice Data | Incomplete Job | No Blower Door Test | Blower Door Indicator = 0 | Either Cost Issue | Any of Five Issues Listed
Indicator of Potential Issue | 0.23 | 0.39 | 0.4 | 0.38 | 0.35 | 0.47
Jobs with Potential
H&S Issues

## Slide 16: Assessing the Problem Methodology
16
Merge jobs with potential H&S issues with the cancelled/deferred jobs spreadsheet
  467 2015 jobs with potential issues
  329 in cancelled/deferred spreadsheet
  91 due to health and safety issues
  Others due to refusal, ineligibility, etc.

## Slide 17: Assessing the Problem Methodology
17
Request 229 job files
  91 cancelled/deferred due to health and safety issues
  138 identified as having a potential health and safety issue, but not in cancelled/deferred spreadsheet
Review job files – audit form, work scope, measure invoice(s)
Assess whether H&S issue prevented work
122 jobs had at least one H&S issue (12% of all 2015 jobs)

## Slide 18: Frequency of H&S Issues
18
Chart: Percentage of Flagged 2015 Jobs with H&S Issues
| No Invoice Data | Incomplete Job | No Blower Door Test | Blower Door Indicator = 0 | Either Cost Issue | Cancelled Jobs | Any of Six Issues Listed
Percent of H&S Issues | 0.03 | 0.18 | 0.23 | 0.21 | 0.14 | 0.09 | 0.26

## Slide 19: Frequency of Specific Health and Safety Issues
19
Chart: Percentage of Health and Safety Issues In Jobs with At Least One Issue Identified
| Mold or Moisture | Knob and Tube Wiring | Roof Leak | Asbestos/ Vermiculate | Sewage Leak
Percent of H&S Issues | 0.68 | 0.34 | 0.31 | 0.15 | 0.11
Other Issues: | Infestation | Structural Issues
 | Holes in Attic Floor | Clutter

## Slide 20: Current Health and Safety Approach
20

## Slide 21: Health and Safety Remediation Approach
21
Spend up to $650 for owner or renter
Renter – spending usually related to HVAC
Owner – could be roof patch, small amount of mold, etc.
Contractors request additional H&S spending
  Approved based on potential savings

## Slide 22: Health and Safety Repairs
22
Chart: Percentage of 2013-2015 Jobs with H&S Repairs
| Dryer Venting | Miscellaneous | Interior | Kitchen or Bath Exhaust | Roof | Any Repair
Repair Issue | 0.5 | 0.38 | 0.35 | 0.11 | 0.05 | 0.74
Mean Cost | $91 | $392 | $304 | $236 | $167 | $453

## Slide 23: Health and Safety Spending Distribution
23
Repair Issue | Repair Cost (For 2013-2015 Jobs with Repair) |  |  |  |  |  |  | 
 | Mean | Percentile |  |  |  |  |  | 
 |  | Min | 10 | 25 | 50 | 75 | 90 | Max
Dryer Venting | $91 | $10 | $57 | $75 | $90 | $91 | $119 | $635
Miscellaneous | $392 | $0 | $31 | $48 | $102 | $239 | $1,388 | $6,464
Interior | $304 | $8 | $75 | $112 | $153 | $345 | $684 | $2,654
Kitchen or Bath Exhaust | $236 | $28 | $82 | $125 | $202 | $350 | $420 | $1,016
Roof | $167 | $20 | $70 | $85 | $85 | $170 | $370 | $850
Total – Any Repair | $453 | $0 | $80 | $105 | $230 | $440 | $1,025 | $6,625

## Slide 24: LIURP Savings Results
24

## Slide 25: Weather-Normalized Energy Savings
25
2013, 2014, and 2015 jobs
Energy savings based on billing data
3-year analysis to allow for disaggregation
  Pre-treatment usage
  Contractor
  Measures
  Job costs

## Slide 26: Weather-Normalized Gas Savings Analysis
26
Analysis Group | Observations | Usage (ccf) |  | Savings | 
 |  | Pre | Post | ccf | %
2015 | 533 | 1,449 | 1,191 | 258** | 17.8%
2013-2015 | 1,398 | 1,515 | 1,211 | 304** | 20.1%
**Denotes significance at the 99 percent level. |  |  |  |  | 

## Slide 27: Savings by Pre-Treatment Usage
27
Chart: 2013-2015 Job Savings by Pre-Treatment Usage
| <1,000 | 1,001- 1,100 | 1,101- 1,200 | 1,201- 1,300 | 1,301- 1,400 | 1,401- 1,500 | 1,501- 1,600 | 1,601- 1,700 | 1,701- 1,800 | 1,801- 1,900 | 1,901- 2,000 | 2,001- 2,200 | 2,201+
Savings | 159 | 172 | 222 | 245 | 252 | 301 | 313 | 308 | 345 | 410 | 412 | 419 | 629

## Slide 28: Savings by Pre-Treatment Usage
28
Pre-Treatment Usage (ccf) | 2013-2015 Participants |  |  |  |  | 
 | Obs. | Total Cost | Usage (ccf) |  | Savings | 
 |  |  | Pre | Post | ccf | %
<1,000 | 104 | $5,514 | 927 | 767 | 159** | 17.2%
1,001-1,100 | 122 | $4,935 | 1,049 | 877 | 172** | 16.4%
1,101-1,200 | 118 | $5,672 | 1,151 | 929 | 222** | 19.3%
1,201-1,300 | 136 | $5,307 | 1,249 | 1,004 | 245** | 19.6%
1,301-1,400 | 159 | $5,288 | 1,349 | 1,097 | 252** | 18.7%
1,401-1,500 | 125 | $5,574 | 1,448 | 1,147 | 301** | 20.8%
1,501-1,600 | 151 | $5,135 | 1,547 | 1,234 | 313** | 20.2%
1,601-1,700 | 112 | $5,217 | 1,648 | 1,340 | 308** | 18.7%
1,701-1,800 | 89 | $5,130 | 1,746 | 1,402 | 345** | 19.8%
1,801-1,900 | 67 | $5,648 | 1,847 | 1,436 | 410** | 22.2%
1,901-2,000 | 54 | $6,169 | 1,947 | 1,535 | 412** | 21.2%
2,001-2,200 | 60 | $6,408 | 2,082 | 1,663 | 419** | 20.1%
2,201+ | 101 | $7,601 | 2,627 | 1,999 | 629** | 23.9%
**Denotes significance at the 99 percent level. |  |  |  |  |  | 

## Slide 29
29
Chart: 2013-2015 Job Savings by Contractor
| 108 | 75 | 90 | 102 | 83 | 103 | 96 | 77 | 101 | 74 | 28
Savings | 201 | 226 | 233 | 245 | 257 | 275 | 294 | 296 | 310 | 336 | 433
Savings by Contractor

## Slide 30
30
Contractor Code | 2013-2015 Participants |  |  |  |  | 
 | Obs. | Mean Cost | Usage (ccf) |  | Savings | 
 |  |  | Pre | Post | ccf | %
28 | 306 | $8,184 | 1,573 | 1,140 | 433** | 27.5%
83 | 169 | $4,968 | 1,528 | 1,270 | 257** | 16.8%
101 | 121 | $8,322 | 1,478 | 1,168 | 310** | 21.0%
74 | 108 | $7,836 | 1,458 | 1,121 | 336** | 23.1%
96 | 98 | $5,160 | 1,436 | 1,141 | 294** | 20.5%
90 | 96 | $7,046 | 1,420 | 1,187 | 233** | 16.4%
102 | 81 | $5,105 | 1,619 | 1,374 | 245** | 15.1%
77 | 78 | $5,979 | 1,467 | 1,171 | 296** | 20.2%
108 | 76 | $8,052 | 1,317 | 1,116 | 201** | 15.3%
75 | 66 | $5,445 | 1,526 | 1,299 | 226** | 14.8%
103 | 57 | $7,677 | 1,716 | 1,441 | 275** | 16.0%
Others | 142 | $7,852 | 1,558 | 1,306 | 253** | 16.2%
**Denotes significance at the 99 percent level. |  |  |  |  |  | 
Savings by Contractor

## Slide 31: Savings by Total Cost
31
Chart: 2013-2015 Job Savings by Total Cost
| <=$4,000 | $4,001-$6,000 | $6,001-$8,000 | $8,000-$10,000 | >$10,000
Savings | 180 | 233 | 318 | 367 | 458

## Slide 32: Savings by Total Cost
32
Total Cost | Obs. | Mean Total Cost | Usage (ccf) |  | Savings | 
 |  |  | Pre | Post | ccf | %
<=$4,000 | 264 | $2,806 | 1,492 | 1,312 | 180** | 12.1%
$4,001-$6,000 | 336 | $5,112 | 1,505 | 1,272 | 233** | 15.5%
$6,001-$8,000 | 320 | $6,970 | 1,511 | 1,192 | 318** | 21.1%
$8,000-$10,000 | 230 | $8,898 | 1,504 | 1,137 | 367** | 24.4%
>$10,000 | 248 | $12,288 | 1,571 | 1,113 | 458** | 29.2%
**Denotes significance at the 99 percent level. |  |  |  |  |  | 

## Slide 33: Savings by Total Cost
33
Chart: 2013-2015 Job Savings by Total Cost – Excluding Heating System Replacement Costs
| <=$4,000 | $4,001-$6,000 | $6,001-$8,000 | >$8000
Savings | 234 | 278 | 357 | 410

## Slide 34: Savings by Cost – Excluding Heating System Replacement
34
Total Cost (Excluding Heating System Replacement) | 2013-2015 Participants |  |  |  |  | 
 | Obs. | Mean Total Cost | Usage (ccf) |  | Savings | 
 |  |  | Pre | Post | ccf | %
<=$4,000 | 451 | $2,434 | 1,505 | 1,271 | 234** | 15.5%
$4,001-$6,000 | 374 | $5,101 | 1,497 | 1,218 | 278** | 18.6%
$6,001-$8,000 | 353 | $6,966 | 1,488 | 1,131 | 357** | 24.0%
>$8,000 | 220 | $11,341 | 1,612 | 1,202 | 410** | 25.4%
**Denotes significance at the 99 percent level. |  |  |  |  |  | 

## Slide 35: Savings by Measures Installed
35
Measure Installed | 2013-2015 Participants |  |  |  |  | 
 | Observations | Mean Total Cost | Usage (ccf) |  | Savings | 
 |  |  | Pre | Post | ccf | %
Blower Door Test |  |  |  |  |  | 
Yes | 1,282 | $7,188 | 1,513 | 1,204 | 310** | 20.5%
No | 116 | $4,902 | 1,537 | 1,291 | 247** | 16.0%
Blower Door Guided Air Sealing |  |  |  |  |  | 
Yes | 618 | $7,110 | 1,517 | 1,195 | 323** | 21.3%
No | 780 | $6,909 | 1,514 | 1,224 | 290** | 19.2%
**Denotes significance at the 99 percent level. |  |  |  |  |  | 

## Slide 36: Savings by Measures Installed (cont.)
36
Measure Installed | 2013-2015 Participants |  |  |  |  | 
 | Observations | Mean Total Cost | Usage (ccf) |  | Savings | 
 |  |  | Pre | Post | ccf | %
Blower Door Guided Air Sealing & Insulation |  |  |  |  |  | 
Yes | 563 | $7,403 | 1,513 | 1,173 | 339** | 22.4%
No | 835 | $6,724 | 1,517 | 1,236 | 281** | 18.5%
Heating System Repair |  |  |  |  |  | 
Yes | 390 | $7,394 | 1,467 | 1,191 | 275** | 18.8%
No | 1,008 | $6,845 | 1,534 | 1,218 | 316** | 20.6%
Heating System Replacement |  |  |  |  |  | 
Yes | 599 | $8,762 | 1,526 | 1,133 | 392** | 25.7%
No | 799 | $5,676 | 1,508 | 1,269 | 239** | 15.8%
**Denotes significance at the 99 percent level. |  |  |  |  |  | 

## Slide 37: Savings by Measures Installed (cont.)
37
Measure Installed | 2013-2015 Participants |  |  |  |  | 
 | Observations | Mean Total Cost | Usage (ccf) |  | Savings | 
 |  |  | Pre | Post | ccf | %
Duct Work |  |  |  |  |  | 
Yes | 546 | $7,097 | 1,458 | 1,115 | 343** | 23.5%
No | 852 | $6,935 | 1,552 | 1,272 | 280** | 18.0%
Health & Safety Repairs |  |  |  |  |  | 
Yes | 1,028 | $7,433 | 1,508 | 1,190 | 317** | 21.0%
No | 370 | $5,789 | 1,537 | 1,267 | 270** | 17.5%
**Denotes significance at the 99 percent level. |  |  |  |  |  | 

## Slide 38
38
Savings by
Leakage Reduction
Chart: 2015 Job Savings by CFM50 Reduction
| <=500 | 500-1,000 | 1,001-2,000 | >2,000 | All
Savings | 213 | 257 | 300 | 343 | 273

## Slide 39: Savings by Leakage Reduction
39
CFM50 Reduction | 2015 Participants |  |  |  |  | 
 | Obs. | Mean Total Cost | Usage (ccf) |  | Savings | 
 |  |  | Pre | Post | ccf | %
<=500 | 140 | $7,183 | 1,437 | 1,224 | 213** | 14.8%
500-1,000 | 80 | $6,771 | 1,430 | 1,174 | 257** | 17.9%
1,001-2,000 | 111 | $7,373 | 1,408 | 1,107 | 300** | 21.3%
>2,000 | 96 | $8,880 | 1,585 | 1,242 | 343** | 21.6%
All | 427 | $7,537 | 1,461 | 1,188 | 273** | 18.7%
**Denotes significance at the 99 percent level. |  |  |  |  |  | 

## Slide 40: Potential Savings for Homes with Health and Safety Problems
40

## Slide 41: Potential Savings
41
Predict energy savings
Regression analysis
Job-related factors

## Slide 42: Regression Analysis 2013 - 2015
42
Variable | 2013-2015 Participants (1,372 observations) |  | 
 | Coefficient | 95% Confidence Interval | 
Pre-Treatment Usage (ccf) | 0.30 | 0.27 | 0.32
Home Age | -1.06 | -1.51 | -0.61
Square Feet | -0.09 | -0.11 | -0.07
Blower Door and Air Sealing Cost | 0.05 | 0.04 | 0.05
Heating System Replaced (yes/no) | 154.56 | 131.84 | 177.28
Duct Sealing (yes/no) | 55.80 | 32.41 | 79.19
Contractor #74 | 79.58 | 36.48 | 122.67
Contractor #77 | 73.69 | 23.52 | 123.86
Contractor # 102 | -72.10 | -119.97 | -24.22
Contractor # 103 | -106.37 | -162.50 | -50.24
Constant | -73.01 | -135.24 | -10.79

## Slide 43: Decision Framework for Additional Health and Safety Investments
43

## Slide 44: Modelled Scenarios Decision Framework
44
Determine how much to spend on health and safety remediation
Modelled range of pre-treatment usage, home age, size, and measure investments
Model calculates
  Predicted ccf savings
  % savings
  Present discounted value of savings
  Max that can be spent on H&S

## Slide 45: Model Assumptions
45
12-year measure life
Gas price at time of study: $1.04723/therm
5% discount rate
Also shows results with no discounting

## Slide 46: Model Scenarios – Scenario 1
46
User Entered Fields | Scenario 1
Pre-Treatment Therms | 1,500
Home Age | 50
Square Feet | 1,500
Air seal + Insulation Cost | $800
Heat Sys Replace (yes=1) | 0
Duct Sealing (yes=1) | 0
Contractor 74 | 0
Contractor 102 | 0
Contractor 77 | 0
Contractor 103 | 0
Heat Sys Cost | 0
Other Non H&S Costs | $800
Calculated Fields (5% Discount) | Scenario 1
Annual Savings (Therms) | 214
Calculated % Savings | 14%
PDV Savings (Therms) | 1,897
Max Spending | $1,986
Total Non H&S Costs | $1,600
H&S Allowance | $386
Calculated Fields (No Discount) | Scenario 1
12-Year Savings (Therms) | 2,568
Max Spending | $2,689
H&S Allowance | $1,089

## Slide 47: Model Scenarios – Scenario 2
47
User Entered Fields | Scenario 2
Pre-Treatment Therms | 1,600
Home Age | 30
Square Feet | 1,250
Air seal + Insulation Cost | $1,400
Heat Sys Replace (yes=1) | 0
Duct Sealing (yes=1) | 1
Contractor 74 | 0
Contractor 102 | 1
Contractor 77 | 0
Contractor 103 | 0
Heat Sys Cost | $0
Other Non H&S Costs | $800
Calculated Fields (5% Discount) | Scenario 2
Annual Savings (Therms) | 301
Calculated % Savings | 19%
PDV Savings (Therms) | 2,672
Max Spending | $2,798
Total Non H&S Costs | $2,200
H&S Allowance | $598
Calculated Fields (No Discount) | Scenario 2
12-Year Savings (Therms) | 3,618
Max Spending | $3,789
H&S Allowance | $1,589

## Slide 48: Model Scenarios – Scenario 3
48
User Entered Fields | Scenario 3
Pre-Treatment Therms | 2,500
Home Age | 100
Square Feet | 2,000
Air seal + Insulation Cost | $1,000
Heat Sys Replace (yes=1) | 1
Duct Sealing (yes=1) | 0
Contractor 74 | 0
Contractor 102 | 0
Contractor 77 | 0
Contractor 103 | 0
Heat Sys Cost | $3,500
Other Non H&S Costs | $1,000
Calculated Fields (5% Discount) | Scenario 3
Annual Savings (Therms) | 578
Calculated % Savings | 23%
PDV Savings (Therms) | 5,126
Max Spending | $5,368
Total Non H&S Costs | $5,500
H&S Allowance | -$132
Calculated Fields (No Discount) | Scenario 3
12-Year Savings (Therms) | 6,940
Max Spending | $7,267
H&S Allowance | $1,767

## Slide 49: Model Scenarios – Scenario 4
49
User Entered Fields | Scenario 4
Pre-Treatment Therms | 3,800
Home Age | 100
Square Feet | 3,200
Air seal + Insulation Cost | $2,700
Heat Sys Replace (yes=1) | 1
Duct Sealing (yes=1) | 1
Contractor 74 | 1
Contractor 102 | 0
Contractor 77 | 0
Contractor 103 | 0
Heat Sys Cost | $3,500
Other Non H&S Costs | $1,000
Calculated Fields (5% Discount) | Scenario 4
Annual Savings (Therms) | 1,075
Calculated % Savings | 28%
PDV Savings (Therms) | 9,527
Max Spending | $9,977
Total Non H&S Costs | $7,200
H&S Allowance | $2,777
Calculated Fields (No Discount) | Scenario 4
12-Year Savings (Therms) | 12,898
Max Spending | $13,507
H&S Allowance | $6,307

## Slide 50: Model Scenarios – Scenario 5
50
User Entered Fields | Scenario 5
Pre-Treatment Therms | 5,000
Home Age | 100
Square Feet | 3,200
Air seal + Insulation Cost | $5,000
Heat Sys Replace (yes=1) | 1
Duct Sealing (yes=1) | 1
Contractor 74 | 0
Contractor 102 | 0
Contractor 77 | 1
Contractor 103 | 0
Heat Sys Cost | $3,500
Other Non H&S Costs | $2,000
Calculated Fields (5% Discount) | Scenario 5
Annual Savings (Therms) | 1,536
Calculated % Savings | 31%
PDV Savings (Therms) | 13,615
Max Spending | $14,258
Total Non H&S Costs | $10,500
H&S Allowance | $3,758
Calculated Fields (No Discount) | Scenario 5
12-Year Savings (Therms) | 18,434
Max Spending | $19,305
H&S Allowance | $8,805

## Slide 51: Summary and Recommendations
51

## Slide 52: Summary and Recommendations
52
Potential to spend more on health and safety
  Still achieve cost-effective savings
  For homes with high pre-treatment usage
Potential results
  High energy savings
  Reduced costs for ratepayers for CAP participants
  Increased affordability when customer leaves CAP
Recommendation
  Pilot approach for high-usage homes with significant H&S barriers
  Assess savings

## Slide 53: APPENDIX: ADDITIONAL DATA
53

## Slide 54: Measure Costs – Individual Measures
54
Measures | Mean | Min | Percentile |  |  |  |  | Max
 |  |  | P10 | P25 | P50 | P75 | P90 | 
Blower Door Air Sealing | $147 | $0 | $0 | $0 | $0 | $150 | $424 | $3,395
Insulation | $2,012 | $0 | $0 | $302 | $1,686 | $3,260 | $4,664 | $10,514
BD Air Seal+Insul | $2,159 | $0 | $0 | $487 | $1,850 | $3,439 | $4,817 | $10,854
Duct Sealing | $84 | $0 | $0 | $0 | $0 | $89 | $180 | $6,700
Heating System Repair | $162 | $0 | $0 | $0 | $0 | $80 | $529 | $7,269
Heating System Replacement | $1,557 | $0 | $0 | $0 | $0 | $2,950 | $4,550 | $10,375
Health and Safety Costs | $333 | $0 | $0 | $0 | $140 | $324 | $774 | $6,625

## Slide 55
55
Measures | Mean | Min | Percentile |  |  |  |  | Max
 |  |  | P10 | P25 | P50 | P75 | P90 | 
Total Costs – Air Sealing –Insulation | $4,839 | $0 | $1,801 | $2,770 | $4,293 | $6,376 | $8,384 | $20,302
Total Costs – Air Sealing – Insulation – Duct Sealing | $4,755 | $0 | $1,781 | $2,688 | $4,226 | $6,285 | $8,296 | $20,302
Total Costs – Health & Safety | $6,664 | $0 | $2,875 | $4,387 | $6,333 | $8,583 | $10,685 | $23,390
Total Costs | $6,998 | $0 | $3,056 | $4,656 | $6,592 | $8,930 | $11,258 | $23,597
Measure Costs – Totals

## Slide 56: Jobs with Measure
56
Chart: Percentage of 2013-2015 Jobs with Measure
| Blower Door Air Sealing | Insulation | Duct Sealing | Heating System Repair | Heating System Replacement | Health & Safety
Percentage of Jobs with Measure | 0.44 | 0.8 | 0.39 | 0.23 | 0.43 | 0.74

## Slide 57: Measure Costs Jobs with Measure
57
Measures | Cost Statistics for 2013- 2015 Jobs with Measure |  |  |  |  | 
 | Mean | P10 | P25 | P50 | P75 | P90
Blower Door Air Sealing | $334 | $75 | $150 | $170 | $377 | $725
Insulation | $2,520 | $483 | $1,151 | $2,292 | $3,655 | $4,883
Duct Sealing | $215 | $65 | $85 | $134 | $180 | $381
Heating System Repair | $580 | $80 | $175 | $361 | $696 | $1,361
Heating System Replacement | $3,635 | $2,483 | $2,760 | $3,162 | $4,458 | $5,560
Health & Safety | $453 | $80 | $105 | $230 | $440 | $1,025
Total Costs | $7,013 | $3,094 | $4,688 | $6,602 | $8,946 | $11,258