## Slide 1: Health and Safety Investments to Increase Energy-Saving Opportunities
Jackie Berger, APPRISE
2018 Summer Study on Energy Efficiency in Buildings
August 15, 2018

## Slide 2: Presentation Overview
2
Assessing the Problem
Current Health and Safety Investments
LIURP Savings Results
Decision Framework for Additional Health and Safety Investments
Columbia Gas LIURP Background

## Slide 3: Columbia Gas Low-Income Programs
Pennsylvania Utility Mandated Programs
  CAP, LIURP, CARES, Hardship Fund
  LIURP mandated in 1988
Targets CAP customers to reduce ratepayer subsidy
Annual Budget $4,750,000
500 – 550 homes completed annually
Company administered, contractor installations
11 contractors did >50 jobs over 3-year period
3

## Slide 4: Assessing the problem
4

## Slide 5: Low-Income EE Challenge
5
Low-Income Energy Efficiency
Increased challenges serving households
Significant health and safety issues
Prevent installation of major measures
Lost potential for high-usage customers
Health and Safety Investments
Where/when can additional cost-effective investments be made?
How much can cost-effectively be spent on health & safety?

## Slide 6: Assessing the Problem Methodology
6
Analyze 2015 LIURP Database
  Initial indicators of health and safety issues that prevented work
Review cancelled job spreadsheet
Review job paperwork for 229 jobs
  Audit form, work scope, measure invoice(s)
  122 jobs had at least one H&S issue that prevented work
  12% of all 2015 jobs

## Slide 7: Frequency of Specific Health and Safety Issues
7
Chart: Percentage of Health and Safety Issues In Jobs with At Least One Issue Identified
| Mold or Moisture | Knob and Tube Wiring | Roof Leak | Asbestos/ Vermiculate | Sewage Leak
Percent of H&S Issues | 0.68 | 0.34 | 0.31 | 0.15 | 0.11
Other Issues: | Infestation | Structural Issues
 | Holes in Attic Floor | Clutter

## Slide 8: Health and Safety Remediation Approach
8
Spend up to $650 for owner or renter
Renter – spending usually related to HVAC
Owner – could be roof patch, small amount of mold, etc.
Contractors request additional H&S spending
  Approved based on potential savings

## Slide 9: Health and Safety Repairs
9
Chart: Percentage of 2013-2015 Jobs with H&S Repairs
| Dryer Venting | Miscellaneous | Interior | Kitchen or Bath Exhaust | Roof | Any Repair
Repair Issue | 0.5 | 0.38 | 0.35 | 0.11 | 0.05 | 0.74
Mean Cost | $91 | $392 | $304 | $236 | $167 | $453

## Slide 10: LIURP Savings Results
10

## Slide 11: Weather-Normalized Energy Savings
11
2013, 2014, and 2015 jobs
Energy savings based on billing data
3-year analysis to allow for disaggregation
  Pre-treatment usage
  Contractor
  Measures
  Job costs

## Slide 12: Weather-Normalized Gas Savings Analysis
12
Analysis Group | Observations | Usage (ccf) |  | Savings | 
 |  | Pre | Post | ccf | %
2015 | 533 | 1,449 | 1,191 | 258** | 17.8%
2013-2015 | 1,398 | 1,515 | 1,211 | 304** | 20.1%
**Denotes significance at the 99 percent level. |  |  |  |  | 

## Slide 13: Savings by Pre-Treatment Usage
13
Chart: 2013-2015 Job Savings by Pre-Treatment Usage
| <1,000 | 1,001- 1,100 | 1,101- 1,200 | 1,201- 1,300 | 1,301- 1,400 | 1,401- 1,500 | 1,501- 1,600 | 1,601- 1,700 | 1,701- 1,800 | 1,801- 1,900 | 1,901- 2,000 | 2,001- 2,200 | 2,201+
Savings | 159 | 172 | 222 | 245 | 252 | 301 | 313 | 308 | 345 | 410 | 412 | 419 | 629

## Slide 14
14
Chart: 2013-2015 Job Savings by Contractor
| 108 | 75 | 90 | 102 | 83 | 103 | 96 | 77 | 101 | 74 | 28
Savings | 201 | 226 | 233 | 245 | 257 | 275 | 294 | 296 | 310 | 336 | 433
Savings by Contractor

## Slide 15: Savings by Total Cost
15
Chart: 2013-2015 Job Savings by Total Cost
| <=$4,000 | $4,001-$6,000 | $6,001-$8,000 | $8,000-$10,000 | >$10,000
Savings | 180 | 233 | 318 | 367 | 458

## Slide 16
16
Savings by
Leakage Reduction
Chart: 2015 Job Savings by CFM50 Reduction
| <=500 | 500-1,000 | 1,001-2,000 | >2,000
Savings | 213 | 257 | 300 | 343

## Slide 17: Decision Framework for Additional Health and Safety Investments
17

## Slide 18: Regression Analysis 2013 - 2015
18
Variable | 2013-2015 Participants (1,372 observations) |  | 
 | Coefficient | 95% Confidence Interval | 
Pre-Treatment Usage (ccf) | 0.30 | 0.27 | 0.32
Home Age | -1.06 | -1.51 | -0.61
Square Feet | -0.09 | -0.11 | -0.07
Blower Door and Air Sealing Cost | 0.05 | 0.04 | 0.05
Heating System Replaced (yes/no) | 154.56 | 131.84 | 177.28
Duct Sealing (yes/no) | 55.80 | 32.41 | 79.19
Contractor #74 | 79.58 | 36.48 | 122.67
Contractor #77 | 73.69 | 23.52 | 123.86
Contractor # 102 | -72.10 | -119.97 | -24.22
Contractor # 103 | -106.37 | -162.50 | -50.24
Constant | -73.01 | -135.24 | -10.79

## Slide 19: Decision Framework
19
Determine $ to spend on health and safety
Model assumptions
  12-year measure life
  Gas price at time of study: $1.04723/therm
  5% discount rate
Model calculates
  Predicted ccf savings & % savings
  Present discounted value of savings
  Max that can be spent on H&S

## Slide 20: Model Scenarios – Scenario 1
20
User Entered Fields | Scenario 1
Pre-Treatment Therms | 1,500
Home Age | 50
Square Feet | 1,500
Air seal + Insulation Cost | $800
Heat Sys Replace (yes=1) | 0
Duct Sealing (yes=1) | 0
Contractor 74 | 0
Contractor 102 | 0
Contractor 77 | 0
Contractor 103 | 0
Heat Sys Cost | 0
Other Non H&S Costs | $800
Calculated Fields (5% Discount) | Scenario 1
Annual Savings (Therms) | 214
Calculated % Savings | 14%
PDV Savings (Therms) | 1,897
Max Spending | $1,986
Total Non H&S Costs | $1,600
H&S Allowance | $386
Calculated Fields (No Discount) | Scenario 1
12-Year Savings (Therms) | 2,568
Max Spending | $2,689
H&S Allowance | $1,089

## Slide 21: Model Scenarios – Scenario 2
21
User Entered Fields | Scenario 2
Pre-Treatment Therms | 1,600
Home Age | 30
Square Feet | 1,250
Air seal + Insulation Cost | $1,400
Heat Sys Replace (yes=1) | 0
Duct Sealing (yes=1) | 1
Contractor 74 | 0
Contractor 102 | 1
Contractor 77 | 0
Contractor 103 | 0
Heat Sys Cost | $0
Other Non H&S Costs | $800
Calculated Fields (5% Discount) | Scenario 2
Annual Savings (Therms) | 301
Calculated % Savings | 19%
PDV Savings (Therms) | 2,672
Max Spending | $2,798
Total Non H&S Costs | $2,200
H&S Allowance | $598
Calculated Fields (No Discount) | Scenario 2
12-Year Savings (Therms) | 3,618
Max Spending | $3,789
H&S Allowance | $1,589

## Slide 22: Model Scenarios – Scenario 3
22
User Entered Fields | Scenario 3
Pre-Treatment Therms | 2,500
Home Age | 100
Square Feet | 2,000
Air seal + Insulation Cost | $1,000
Heat Sys Replace (yes=1) | 1
Duct Sealing (yes=1) | 0
Contractor 74 | 0
Contractor 102 | 0
Contractor 77 | 0
Contractor 103 | 0
Heat Sys Cost | $3,500
Other Non H&S Costs | $1,000
Calculated Fields (5% Discount) | Scenario 3
Annual Savings (Therms) | 578
Calculated % Savings | 23%
PDV Savings (Therms) | 5,126
Max Spending | $5,368
Total Non H&S Costs | $5,500
H&S Allowance | -$132
Calculated Fields (No Discount) | Scenario 3
12-Year Savings (Therms) | 6,940
Max Spending | $7,267
H&S Allowance | $1,767

## Slide 23: Model Scenarios – Scenario 4
23
User Entered Fields | Scenario 4
Pre-Treatment Therms | 3,800
Home Age | 100
Square Feet | 3,200
Air seal + Insulation Cost | $2,700
Heat Sys Replace (yes=1) | 1
Duct Sealing (yes=1) | 1
Contractor 74 | 1
Contractor 102 | 0
Contractor 77 | 0
Contractor 103 | 0
Heat Sys Cost | $3,500
Other Non H&S Costs | $1,000
Calculated Fields (5% Discount) | Scenario 4
Annual Savings (Therms) | 1,075
Calculated % Savings | 28%
PDV Savings (Therms) | 9,527
Max Spending | $9,977
Total Non H&S Costs | $7,200
H&S Allowance | $2,777
Calculated Fields (No Discount) | Scenario 4
12-Year Savings (Therms) | 12,898
Max Spending | $13,507
H&S Allowance | $6,307

## Slide 24: Model Scenarios – Scenario 5
24
User Entered Fields | Scenario 5
Pre-Treatment Therms | 5,000
Home Age | 100
Square Feet | 3,200
Air seal + Insulation Cost | $5,000
Heat Sys Replace (yes=1) | 1
Duct Sealing (yes=1) | 1
Contractor 74 | 0
Contractor 102 | 0
Contractor 77 | 1
Contractor 103 | 0
Heat Sys Cost | $3,500
Other Non H&S Costs | $2,000
Calculated Fields (5% Discount) | Scenario 5
Annual Savings (Therms) | 1,536
Calculated % Savings | 31%
PDV Savings (Therms) | 13,615
Max Spending | $14,258
Total Non H&S Costs | $10,500
H&S Allowance | $3,758
Calculated Fields (No Discount) | Scenario 5
12-Year Savings (Therms) | 18,434
Max Spending | $19,305
H&S Allowance | $8,805

## Slide 25: Summary and Recommendations
25

## Slide 26: Summary and Recommendations
26
Potential to spend more on health and safety
  Still achieve cost-effective savings
  For homes with high pre-treatment usage
Potential results
  High energy savings
  Reduced costs for ratepayers for CAP participants
  Increased affordability when customer leaves CAP
Recommendation
  Pilot approach for high-usage homes with significant H&S barriers
  Assess savings

## Slide 27: APPENDIX: ADDITIONAL DATA
27

## Slide 28: Health and Safety Spending Distribution
28
Repair Issue | Repair Cost (For 2013-2015 Jobs with Repair) |  |  |  |  |  |  | 
 | Mean | Percentile |  |  |  |  |  | 
 |  | Min | 10 | 25 | 50 | 75 | 90 | Max
Dryer Venting | $91 | $10 | $57 | $75 | $90 | $91 | $119 | $635
Miscellaneous | $392 | $0 | $31 | $48 | $102 | $239 | $1,388 | $6,464
Interior | $304 | $8 | $75 | $112 | $153 | $345 | $684 | $2,654
Kitchen or Bath Exhaust | $236 | $28 | $82 | $125 | $202 | $350 | $420 | $1,016
Roof | $167 | $20 | $70 | $85 | $85 | $170 | $370 | $850
Total – Any Repair | $453 | $0 | $80 | $105 | $230 | $440 | $1,025 | $6,625

## Slide 29: Savings by Pre-Treatment Usage
29
Pre-Treatment Usage (ccf) | 2013-2015 Participants |  |  |  |  | 
 | Obs. | Total Cost | Usage (ccf) |  | Savings | 
 |  |  | Pre | Post | ccf | %
<1,000 | 104 | $5,514 | 927 | 767 | 159** | 17.2%
1,001-1,100 | 122 | $4,935 | 1,049 | 877 | 172** | 16.4%
1,101-1,200 | 118 | $5,672 | 1,151 | 929 | 222** | 19.3%
1,201-1,300 | 136 | $5,307 | 1,249 | 1,004 | 245** | 19.6%
1,301-1,400 | 159 | $5,288 | 1,349 | 1,097 | 252** | 18.7%
1,401-1,500 | 125 | $5,574 | 1,448 | 1,147 | 301** | 20.8%
1,501-1,600 | 151 | $5,135 | 1,547 | 1,234 | 313** | 20.2%
1,601-1,700 | 112 | $5,217 | 1,648 | 1,340 | 308** | 18.7%
1,701-1,800 | 89 | $5,130 | 1,746 | 1,402 | 345** | 19.8%
1,801-1,900 | 67 | $5,648 | 1,847 | 1,436 | 410** | 22.2%
1,901-2,000 | 54 | $6,169 | 1,947 | 1,535 | 412** | 21.2%
2,001-2,200 | 60 | $6,408 | 2,082 | 1,663 | 419** | 20.1%
2,201+ | 101 | $7,601 | 2,627 | 1,999 | 629** | 23.9%
**Denotes significance at the 99 percent level. |  |  |  |  |  | 

## Slide 30
30
Contractor Code | 2013-2015 Participants |  |  |  |  | 
 | Obs. | Mean Cost | Usage (ccf) |  | Savings | 
 |  |  | Pre | Post | ccf | %
28 | 306 | $8,184 | 1,573 | 1,140 | 433** | 27.5%
83 | 169 | $4,968 | 1,528 | 1,270 | 257** | 16.8%
101 | 121 | $8,322 | 1,478 | 1,168 | 310** | 21.0%
74 | 108 | $7,836 | 1,458 | 1,121 | 336** | 23.1%
96 | 98 | $5,160 | 1,436 | 1,141 | 294** | 20.5%
90 | 96 | $7,046 | 1,420 | 1,187 | 233** | 16.4%
102 | 81 | $5,105 | 1,619 | 1,374 | 245** | 15.1%
77 | 78 | $5,979 | 1,467 | 1,171 | 296** | 20.2%
108 | 76 | $8,052 | 1,317 | 1,116 | 201** | 15.3%
75 | 66 | $5,445 | 1,526 | 1,299 | 226** | 14.8%
103 | 57 | $7,677 | 1,716 | 1,441 | 275** | 16.0%
Others | 142 | $7,852 | 1,558 | 1,306 | 253** | 16.2%
**Denotes significance at the 99 percent level. |  |  |  |  |  | 
Savings by Contractor

## Slide 31: Savings by Total Cost
31
Total Cost | Obs. | Mean Total Cost | Usage (ccf) |  | Savings | 
 |  |  | Pre | Post | ccf | %
<=$4,000 | 264 | $2,806 | 1,492 | 1,312 | 180** | 12.1%
$4,001-$6,000 | 336 | $5,112 | 1,505 | 1,272 | 233** | 15.5%
$6,001-$8,000 | 320 | $6,970 | 1,511 | 1,192 | 318** | 21.1%
$8,000-$10,000 | 230 | $8,898 | 1,504 | 1,137 | 367** | 24.4%
>$10,000 | 248 | $12,288 | 1,571 | 1,113 | 458** | 29.2%
**Denotes significance at the 99 percent level. |  |  |  |  |  | 

## Slide 32: Savings by Leakage Reduction
32
CFM50 Reduction | 2015 Participants |  |  |  |  | 
 | Obs. | Mean Total Cost | Usage (ccf) |  | Savings | 
 |  |  | Pre | Post | ccf | %
<=500 | 140 | $7,183 | 1,437 | 1,224 | 213** | 14.8%
500-1,000 | 80 | $6,771 | 1,430 | 1,174 | 257** | 17.9%
1,001-2,000 | 111 | $7,373 | 1,408 | 1,107 | 300** | 21.3%
>2,000 | 96 | $8,880 | 1,585 | 1,242 | 343** | 21.6%
All | 427 | $7,537 | 1,461 | 1,188 | 273** | 18.7%
**Denotes significance at the 99 percent level. |  |  |  |  |  | 

## Slide 33: Measure Costs – Individual Measures
33
Measures | Mean | Min | Percentile |  |  |  |  | Max
 |  |  | P10 | P25 | P50 | P75 | P90 | 
Blower Door Air Sealing | $147 | $0 | $0 | $0 | $0 | $150 | $424 | $3,395
Insulation | $2,012 | $0 | $0 | $302 | $1,686 | $3,260 | $4,664 | $10,514
BD Air Seal+Insul | $2,159 | $0 | $0 | $487 | $1,850 | $3,439 | $4,817 | $10,854
Duct Sealing | $84 | $0 | $0 | $0 | $0 | $89 | $180 | $6,700
Heating System Repair | $162 | $0 | $0 | $0 | $0 | $80 | $529 | $7,269
Heating System Replacement | $1,557 | $0 | $0 | $0 | $0 | $2,950 | $4,550 | $10,375
Health and Safety Costs | $333 | $0 | $0 | $0 | $140 | $324 | $774 | $6,625

## Slide 34
34
Measures | Mean | Min | Percentile |  |  |  |  | Max
 |  |  | P10 | P25 | P50 | P75 | P90 | 
Total Costs – Air Sealing –Insulation | $4,839 | $0 | $1,801 | $2,770 | $4,293 | $6,376 | $8,384 | $20,302
Total Costs – Air Sealing – Insulation – Duct Sealing | $4,755 | $0 | $1,781 | $2,688 | $4,226 | $6,285 | $8,296 | $20,302
Total Costs – Health & Safety | $6,664 | $0 | $2,875 | $4,387 | $6,333 | $8,583 | $10,685 | $23,390
Total Costs | $6,998 | $0 | $3,056 | $4,656 | $6,592 | $8,930 | $11,258 | $23,597
Measure Costs – Totals

## Slide 35: Jobs with Measure
35
Chart: Percentage of 2013-2015 Jobs with Measure
| Blower Door Air Sealing | Insulation | Duct Sealing | Heating System Repair | Heating System Replacement | Health & Safety
Percentage of Jobs with Measure | 0.44 | 0.8 | 0.39 | 0.23 | 0.43 | 0.74

## Slide 36: Measure Costs Jobs with Measure
36
Measures | Cost Statistics for 2013- 2015 Jobs with Measure |  |  |  |  | 
 | Mean | P10 | P25 | P50 | P75 | P90
Blower Door Air Sealing | $334 | $75 | $150 | $170 | $377 | $725
Insulation | $2,520 | $483 | $1,151 | $2,292 | $3,655 | $4,883
Duct Sealing | $215 | $65 | $85 | $134 | $180 | $381
Heating System Repair | $580 | $80 | $175 | $361 | $696 | $1,361
Heating System Replacement | $3,635 | $2,483 | $2,760 | $3,162 | $4,458 | $5,560
Health & Safety | $453 | $80 | $105 | $230 | $440 | $1,025
Total Costs | $7,013 | $3,094 | $4,688 | $6,602 | $8,946 | $11,258