## Slide 1: Testing Really Matters for Technical Reference Manuals The Need for Evaluation Research to Assess, Calibrate, and Update TRMs
Jackie Berger
Home Performance Conference
April 3, 2019

## Slide 2: Projection
2

## Slide 3: Bad Forecast?
3

## Slide 4: Projections
4
Time Magazine, November 8, 2016
Associated Press
Nate Silver
Princeton Election Consortium
Moody’s Analytics
…With just hours to go until the polls close on Election Day, pollsters and predictors have released their final maps of the 2016 election—and most agree that Hillary Clinton will win, but no one agrees by how much.

## Slide 5: November 9, 2016
5

## Slide 6: Overview
TRM Overview, Uses, Importance
TRM Advantages and Disadvantages
TRM and Billing Analysis Examples
Summary and Recommendations
Additional Research Approaches
6

## Slide 7: Technical Reference Manuals
7

## Slide 8: What are TRMs?
Equations used to calculate energy or demand savings that results from an efficiency measure.
Use of newly installed measure compare to a baseline.
8

## Slide 9: Baseline
What is the baseline?
Existing equipment
Current code requirements or standard equipment
Intermediate
Existing equipment for remaining life in existing equipment
Standard equipment for rest of the life of the new measure
Low-Income may continue to use equipment past the expected life
9

## Slide 10: TRM Examples
NJ 2018 TRM
Lighting Savings (kWh/yr) = * HRS * (1+HVACE)
Lighting Savings (kWh/yr) =(𝑊𝑎𝑡𝑡𝑠∗𝑄𝑇𝑌)𝐵𝐿" − " (𝑊𝑎𝑡𝑡𝑠∗𝑄𝑇𝑌)𝑃" " /1,000 * HRS * (1+HVACE)
Mid Atlantic 2016 TRM
HE Gas Boiler Savings (MMBTU/yr)=
HE Gas Boiler Savings (MMBTU/yr)= (𝐸𝐹𝐿𝐻ℎ𝑒𝑡∗𝐵𝑡𝑢ℎ∗𝐴𝐹𝑈𝐸𝑒𝑒/𝐴𝐹𝑈𝐸𝑏𝑎𝑠𝑒)/1,000,000
MN 2019 TRM
LF SH Savings (kWh/yr) =
LF SH Savings (kWh/yr) =((〖𝐺𝑃𝑀〗_(𝐵𝐴𝑆𝐸 )−〖𝐺𝑃𝑀〗_𝐿𝑂𝑊 )∗((𝑃𝐻∗𝑆𝑃𝐷∗𝑆𝐿)/𝑆𝑃𝐻)∗365∗𝐷𝑒𝑛𝑠𝑖𝑡𝑦∗𝐶_𝑃∗(𝑇_𝑂𝑈𝑇−𝑇_𝐼𝑁))/(𝑅𝑒𝐸𝑓𝑓∗3,412)
HVACE accounts for interaction, reduces gas heating saved, increases cooling saved
EFLHhet=equivalent full load heating hours
AFUE = efficiency
Gallons per Minute, People in Home, Showers per Day, Shower Length, Showers per Home, Shower Temperature, Groundwater Temperature, Recovery Efficiency (98%)
NJ 2018 TRM
Mid Atlantic 2016 TRM
MN 2019 TRM
10

## Slide 11: TRM Use
11

## Slide 12: How are TRMs Used?
Regulatory Reporting
Non-Energy Impacts
Environmental impacts
Economic impacts
Cost-Effectiveness Calculations
Measure selection
Program implementation or continuation
Program Comparisons
Energy Efficiency Resource Standard (EERS)
Performance incentives & penalties
Decoupling
Lost revenue calculations
Justify program investments
Relative investments and savings
Modifications
12

## Slide 13: TRM Use Regulatory Reporting
13
How are TRM savings referred to?
Understanding of what they mean?
Improvement over number treated or dollars invested?
Overemphasis on TRM as measure of program accomplishment.

## Slide 14: TRM Use Non-Energy Impacts
14
Non-Energy Impacts
Economic Impact
Environmental impact
Many depend upon the level of energy savings achieved
Energy savings translate into increased retail spending
Energy savings translate into reduced greenhouse gas emissions

## Slide 15: TRM Use Cost-Effectiveness
15
Inputs
Program Costs
Energy Savings
Measure Life
Discount Rate
Present Discounted Value of Program Benefits
Present Discounted Value over measure life
Energy Savings
Key input for program and measure-level cost-effectiveness
Energy Savings
Non-Energy Impacts

## Slide 16: TRM Use Program Comparisons
16
Programs
Budget & Spending
Savings Calculation
What is the full set of program offerings?
Do programs cover all market segments?
Do programs cover all energy saving opportunities?
Total budget allocated for energy programs
Extent to which budget is used
Savings
Electric and natural gas savings
Electric demand reduction
TRMs most commonly used
Assessment of how variation in TRMs affect projected savings?
Participants & Measures
Level of program participation
Comprehensiveness of measures included in offerings
Uptake of incentivized measures

## Slide 17: How are TRMs Used? EE Resource Standards
Energy Efficiency Resource Standard (EERS)
Requires utilities to reduce energy consumption by a certain amount
Within designated timeframe
Typically a percentage of usual sales and sometimes a reduction in peak demand
Requirement for Usage Reduction
Utilities are held accountable for what they achieve
Measurement of the energy savings is usually done through deemed savings or TRMs
Focus on outcome rather than input
26 states had EERS in place in January 2017
25 states provided incentives for cost-effective achievement of energy-saving targets
17

## Slide 18: Decoupling
Removes connection between utility revenue and sales volume
May adjust rates regardless of reason for change in revenue
Lost Revenue Adjustment Mechanism (LRAM)
Utility only recovers revenues that are reduced as a result of the energy efficiency programs.
Requires estimate of program savings.
18

## Slide 19: Additional research approaches
19

## Slide 20: Energy Saving Measurement Approaches
Deemed Savings
Technical Reference Manual
Billing Analysis
On-Site Measurement
Important to specify how savings were calculated
Approaches
20

## Slide 21: Billing Analysis
21
Wx
Date
12 Months Pre-Wx
Energy Usage
Weather Normalize
12 Months Post-Wx
Energy Usage
Weather Normalize
Comp.
Group
Wx
Date
13-24 Months Pre-Wx
Energy Usage
Weather Normalize
1-12 Months Pre-Wx
Energy Usage
Weather Normalize
A
B
A-B
Gross Energy Savings
C
D
C-D
Comp. Group Savings
A-B
Net Savings
C-D
Gross Energy Savings
Comparison Group Savings

## Slide 22: Billing Analysis
22
Measure-specific impacts
Usage change = α + β * household characteristics + γ1* measure1 + γ2* measure2 + γ3* measure3 + μ
Needed for Analysis
Variation in measures installed
Significant number of participants with each measure

## Slide 23: TRM advantages and disadvantages
23

## Slide 24: Tradeoffs of Estimation Approaches
24
 | Method |  | 
Factor | Deemed Savings | Technical Reference Manual | Billing Analysis
Accuracy | Lowest | Middle | Highest
Cost | Lowest | Middle | Highest
Data Needs | Lowest | Middle | Highest

## Slide 25: Data Needs for Estimation Approaches
25
Data Element | Is the Data Element Needed for Each Approach |  | 
 | Deemed | TRM | Billing Analysis
Installed Measures | No | Yes | Yes
Pre-Treatment Usage | No | Sometimes | Yes
Post-Treatment Usage | No | No | Yes
Weather Data | No | No | Yes
Comparison Group | No | No | Yes

## Slide 26: TRM Advantages
Data Requirements
Lower Cost
Timeliness
No need to wait for post usage data
Planning & Reporting
No post usage data, weather data, or comparison group data
Less complicated data analysis
26

## Slide 27: TRM Disadvantages Assumptions/Information
Measure Installation Rates
Measure Retention Rates
Pre-Treatment Usage/
Existing Conditions
Measure Effectiveness
Smart thermostat not installed
Removed or broken LED
Hours used for specific measure
Work quality (air sealing comprehensiveness)
27

## Slide 28: TRM Disadvantages
Incorrect TRM Application
Interactions
Shell and heating system
Lighting and heat gain/loss
New Measures
Variation in Savings
Formula
Input values
Not included
Or deemed savings used initially
Difference from one program to another
May relate to TRM rather than effectiveness
28

## Slide 29: TRM examples
29

## Slide 30: PROGRAM 1 example
30

## Slide 31: Low-Income EE Mean Electric & Gas Saved
Chart: Electric Savings
| Electric Non-Heating | Electric Heating
TRM | 1041 | 1715
Billing | 632 | 1179
31
Chart: Gas Savings
| Gas Heating
TRM | 118
Billing | 86

## Slide 32: Low-Income EE Realization Rates
Chart: 
| Electric Non-Heating | Electric Heating | Gas Heating
Realization Rate | 0.61 | 0.69 | 0.73
32

## Slide 33: Low-Income EE Electric Measure Savings
Chart: Mean Electric Savings (kWh)
| Air Sealing | CFLs | Duct Sealing | Hot Water | HVAC | Insulation | Refrigerator | Thermostats
TRM | 199 | 488 | 226 | 178 | 594 | 319 | 1037 | 115
Billing | 445 | 166 | 649 | 446 | 316 | 227 | 330 | 6
33

## Slide 34: Low-Income EE Electric Measure Realization
Chart: Electric Non-Heating Realization Rate
| Air Sealing | CFLs | Duct Sealing | Hot Water | HVAC | Insulation | Refrigerator | Thermostats
Realization Rate | 2.23 | 0.34 | 2.87 | 2.51 | 0.53 | 0.71 | 0.32 | 0.05
34

## Slide 35: Low-Income EE Gas Measure Savings
Chart: Mean Gas Savings (ccf)
| Air Sealing | Duct Sealing | Hot Water | HVAC | Insulation | Thermostats
TRM | 41 | 15 | 10 | 214 | 115 | 27
Billing | 18 | 2 | 1 | 121 | 103 | 20
35

## Slide 36: Low-Income EE Gas Measure Realization
Chart: Gas Measure Realization Rate
| Air Sealing | Duct Sealing | Hot Water | HVAC | Insulation | Thermostats
Realization Rate | 0.44 | 0.13 | 0.1 | 0.57 | 0.9 | 0.74
36

## Slide 37: Low-Income EE Billing Analysis Findings
37
Contractor | Obs. | Mean Net Savings (kWh) | % With Refrigerators Replaced | Refrigerator Replaced | 
 |  |  |  | Yes | No
 |  |  |  | Net Savings (kWh) | 
1 | 885 | 784** | 31% | 877** | 744**
2 | 831 | 392** | 35% | 645** | 255**
3 | 734 | 536** | 50% | 747** | 326**
4 | 508 | 432** | 69% | 554** | 164
5 | 75 | 600** | 40% | 1,122** | 252
6 | 151 | 316** | 47% | 652** | 18
ALL | 3,184 | 542** | 43% | 705** | 417**
Electric Baseload Jobs

## Slide 38: Low-Income EE Billing Analysis Findings
38
Refrigerator | # CFL | Contractor 1 |  |  |  | Other Contractors |  |  |  | Total |  |  | 
 |  | Obs | Mean # CFL | Savings |  | Obs | Mean # CFL | Savings |  | Obs | Mean # CFL | Savings | 
 |  |  |  | kWh | % |  |  | kWh | % |  |  | kWh | %
Yes | 0 | 88 | 0 | 692 | 10% | 252 | 0 | 452 | 6% | 340 | 0 | 514 | 7%
Yes | 1-6 | 56 | 4.3 | 668 | 10% | 194 | 3.8 | 591 | 8% | 250 | 3.9 | 609 | 9%
Yes | 7 + | 127 | 15.9 | 1,096 | 14% | 663 | 16.1 | 764 | 9% | 790 | 16.1 | 818 | 10%
No | 0 | 205 | 0 | 465 | 6% | 434 | 0 | 172 | 2% | 639 | 0 | 266 | 3%
No | 1-6 | 117 | 4 | 480 | 7% | 230 | 3.8 | 199 | 3% | 347 | 3.8 | 294 | 4%
No | 7 + | 292 | 15.5 | 1,045 | 12% | 526 | 15.9 | 333 | 4% | 818 | 15.7 | 587 | 7%

## Slide 39: PROGRAM 2 example
39

## Slide 40: Res High-Efficiency Furnace Replacement
Chart: TRM % Saved
| Furnace | Boiler
% Saved | 0.17 | 0.16
40
Chart: Billing Analysis % Saved
| Furnace | Boiler
% Saved | 0.13 | 0.17
Chart: Realization Rate
| Furnace | Boiler
% Saved | 0.48 | 0.62

## Slide 41: Res High-Efficiency Furnace Replacement
Chart: Pre-Treatment Usage
| Furnace | Boiler
TRM | 1376 | 2153
Billing | 862 | 1186
41

## Slide 42: Res High-Efficiency Furnace Replacement
Chart: 
| Furnace | Boiler
Realization Rate | 1.12 | 0.92
42
TRM updated based on first evaluation findings.

## Slide 43: Res High-Efficiency Furnace Replacement
43
Furnace Capacity | Furnace AFUE | Obs. | Net Estimated Savings | Technical Resource Manual Savings (ccf) | Realization Rate
<70 | 95-<96 | 12 | 86 | 87 | 99%
 | 96-<97 | 32 | 125 | 89 | 140%
 | ≥97 | 2 | 107 | 93 | 115%
70-80 | 95-<96 | 31 | 64 | 112 | 57%
 | 96-<97 | 32 | 81 | 119 | 68%
 | ≥97 | 7 | 58 | 125 | 46%
>80 | 95-<96 | 31 | 112 | 134 | 84%
 | 96-<97 | 20 | 119 | 148 | 80%
 | ≥97 | 3 | -69 | 163 | --
Evaluation 2 Revised TRM

## Slide 44: PROGRAM 3 example
44

## Slide 45: South Jersey Gas Home Performance
45
NJCEP Rebate | Treatment |  |  |  |  | Matched Comparison Group |  |  |  |  | Net Savings | 
 | Obs | Pre | Post | Savings |  | Obs | Pre | Post | Savings |  |  | 
 |  |  |  | ccf | % |  |  |  | ccf | % | ccf | %
<$5,000 | 181 | 920 | 735 | 185 | 20% | 181 | 905 | 899 | 6 | 1% | 179 | 19%
$5,000 | 465 | 849 | 652 | 197 | 23% | 465 | 841 | 861 | -20 | -2% | 217 | 26%
All | 646 | 859 | 675 | 194 | 22% | 646 | 859 | 871 | -13 | -2% | 206 | 24%
Savings estimates statistically significant at 99% level.
NJCEP required at least 25% projected savings for $5,000 rebate.

## Slide 46: South Jersey Gas Home Performance
46
Pre-Period Usage | Treatment |  |  |  |  | Matched Comparison Group |  |  |  |  | Net Savings | 
 | Obs | Pre | Post | Savings |  | Obs | Pre | Post | Savings |  |  | 
 |  |  |  | ccf | % |  |  |  | ccf | % | ccf | %
≤800 ccf | 269 | 662 | 542 | 120* | 18% | 269 | 668 | 689 | -21* | -3% | 141* | 21%
801-1,000 ccf | 204 | 892 | 679 | 213* | 24% | 204 | 875 | 878 | -3 | -<1% | 216* | 24%
>1,000 ccf | 173 | 1,164 | 877 | 287* | 25% | 173 | 1,136 | 1,147 | -11 | -1% | 298* | 26%
All | 646 | 869 | 675 | 194* | 22% | 646 | 859 | 871 | -13* | -2% | 206* | 24%
*Denotes significance at the 99 percent level.

## Slide 47: South Jersey Gas Home Performance
47
Contractor | Treatment |  |  |  |  | Matched Comparison Group |  |  |  |  | Net Savings |  | Average Project Cost
 | Obs | Pre | Post | Savings |  | Obs | Pre | Post | Savings |  |  |  | 
 |  |  |  | ccf | % |  |  |  | ccf | % | ccf | % | 
A | 281 | 890 | 678 | 211* | 23.7% | 281 | 883 | 897 | -14** | -1.6% | 225* | 25.3% | $14,756
B | 98 | 834 | 637 | 198* | 23.7% | 98 | 806 | 812 | -6 | -0.7% | 204* | 24.4% | $17,697
C | 50 | 746 | 615 | 131* | 17.6% | 50 | 742 | 745 | -3 | -0.4% | 135* | 18.0% | $14,839
D | 47 | 901 | 696 | 205* | 22.7% | 47 | 882 | 898 | -16 | -1.9% | 221* | 24.5% | $15,743
E | 34 | 872 | 694 | 178* | 20.4% | 34 | 875 | 920 | -45* | -5.1% | 223* | 25.5% | $15,698
F | 20 | 871 | 732 | 139* | 16.0% | 20 | 864 | 869 | -5 | -0.5% | 144* | 16.5% | $17,190
Other | 116 | 887 | 702 | 184* | 20.8% | 116 | 879 | 890 | -11 | -1.2% | 195* | 22.0% | $15,595
All | 646 | 859 | 675 | 194* | 22.3% | 646 | 859 | 871 | -13*** | -1.5% | 206* | 23.8% | $15,556

## Slide 48: PROGRAM 4 example
48

## Slide 49: All Electric Program
49
Measure | 2011-2015 Jobs | 
 | Source | Mean Annual Savings (kWh)
Insulation – Floor | CT (2016) | 150
 | IL (2016) | 58
Room AC – Early Replacement | CT (2016) | 59
 | PA (2016) | 39
Dehumidifier – Early Replacement | MN (2016) | 136
 | MA (2013-15) | 329
Savings from one Program
Based on Different State TRMs

## Slide 50: PROGRAM 5 example
50

## Slide 51: MN Low-Income Utility Weatherization
 | Delivery | Average Cost | Average TRM Savings (Therms) | Notes
Utility 1 | WAP Agencies | $3,482 | 186 | Consistent with WAP Billing analysis. No data to assess performance of Non-WAP.
Utility 2 | Non-WAP Agencies | $3,122 | 159 | 
Utility 3 | WAP Agencies | $3,354 | 318 | Appears high
Utility 4 | WAP Agencies | $6,689 | 546 | Appears high. No information on pre-treatment usage.
51
Same TRM guidance used.
Basic TRM – no interactions, no pre-treatment condition assessment.
Allowed to use alternative method.
Documentation of calculation not provided.

## Slide 52: Summary and Recommendations
52

## Slide 53: Summary and Recommendations
TRM Use
Savings Estimates Impact
TRM Advantages
TRM Disadvantages
Billing Analysis
Regulatory reporting, cost-benefit analysis, EERS.
Measure selection, program funding, and program continuation, utility incentives or penalties.
Fewer data requirements, faster results, lower cost.
Require many assumptions, often not good predictors of savings, vary by jurisdiction.
Important to use usage data to assess savings.
Provides other important insights for program refinement.
53

## Slide 54: Use Energy Usage Data…
54
Don’t get left out in the cold!